## Slide 1
Motion management in Radiotherapy
Technical and Clinical perspective
Dr Kanhu Charan Patro
MD,DNB(Radiation Oncology),MBA,FICRO,FAROI(USA),PDCR,CEPC
Clinical Director, HOD (Radiation Oncology)
ISRo- Institute of Stereotactic Radiation oncology
Mahatma Gandhi Cancer Hospital & Research Institute, Visakhapatnam
drkcpatro@gmail.com /M- +91-9160470564/ www.drkanhupatro.com
Presented Platform : Global Alliance for Medical Physics Education and Research (GAMPER)

## Slide 2: What is SBRT- THE TRIO?
Ultrahigh dose radiotherapy
Strict immobilization
Motion management

## Slide 5: Organs effected by respiration
Lung
Mediastinum
Heart
Breast
Pancreas
Liver
Kidney
Biliary

## Slide 6: Is lung moves?
Yes
As you go from apex to Lower movement increases
As you go from medial to lateral movement increases

## Slide 7: Motion direction
Superior inferior
Mediolateral
Anteroposterior

## Slide 8: Errors

## Slide 9: MOVEMENT OF TARGET

## Slide 11: SBRT STEPS
MOTION MX

## Slide 12: SBRT WORKFLOW
Simulation
Planning
TX
Delivery
Motion Verification Localization
Motion Management
Delivery

## Slide 13: SBRT – Immobilization

## Slide 14: ORGANS DO NOT FOLLOW STATUE GAME

## Slide 15: Everybody is a king when everything is inside the ring [PTV]

## Slide 16: Motion Management

## Slide 17: Free breathing VS Motion managed

## Slide 18: Is motion being straight forward?
No
Hysterical motion

## Slide 19: GROSSLY
ITV generation
Abdominal compression
Breath holding
Gating
Tracking

## Slide 21: What are the available menu?
ELEKTA – ABC - BREATHHOLD
VARIAN - RPM
CYBERKNIFE – SYNCHRONY
CYBERKNIFE- FUDICAIL
OTHER
  COMPRESSION- ABDOMINAL COMPRESSION
  ITV GENERATION
  VOLUNTARY BREATH HOLD

## Slide 22: ITV GENERATION

## Slide 23: ITV GENERATION
Fluoroscopy mode
4D CT
SLOW CT
MULTIPHASE CT

## Slide 24: 4D CT
4D CT uses a new technology that captures the location and movement of your tumor and the movement of your body's organs over time.
This is valuable for accurately treating tumors located on or near organs that move, such as those in the chest and abdomen.
4D CT describes various techniques for obtaining CT data correlated with patient respiratory phase information so that the changes associated with respiration (or other motion) are displayed.
Phasing the respiratory cycle

## Slide 26: Elekta symmetry Rspiratory phase acquisition

## Slide 30: MULTI PHASE SCAN
INSPIRATION
EXPIRATION
FREE BREATH

## Slide 31: Artefact in motion mx
Slice thickness
Pitch
Phase of respiration

## Slide 32: SLOW CT
Computed tomography scan operated slowly and/or multiple slices taken are averaged, i.e. multiple phases of respiration are recorded by slice
Generally available on most computed tomography scanners.
Loss of resolution, which may lead to tumor blurring and subsequent increase in observer error in tumor and OAR delineation

## Slide 36
Abdominal compression

## Slide 37: Abdominal compression

## Slide 39: Breath holding

## Slide 40: HOLDING
Assists breath-hold by use of a valved spirometer. Often at moderate or deep breath-hold.
Can reduce motion artefacts. Improvements in dose to organs at risk.
Potential for dose escalation compared
with free-breathing technique
Patient selection important; non-compliance of patients with poor respiratory function.
Increase in quality assurance procedures

## Slide 42: ELEKTA ABC
Active breath coordinator
Based on breath hold
During breath hold treatment
Works like spirometry
Needs good lung function

## Slide 43: Nose and mouth piece

## Slide 44: Green is the beam on

## Slide 45
Elekta ABC

## Slide 46: VOLUNTARY BREATH HOLD USING WIRELESS DOOR BELL

## Slide 47: GATING

## Slide 48: MIDDLE- BEAM GATING

## Slide 49
Particular phase
ITV

## Slide 50: GATING
Delivery of radiation within a specified part of the patient’s breathing cycle termed ‘the gate’.
Phase or amplitude based.
Uses external respiration signal e.g. infrared, spirometry, thermistors or internal fiducials. internal fiducials.
Imaging and treatment synchronised with patient’s breathing cycle

## Slide 52: PHASE BASED TREATMENT- CHOOSING PART OF DUTY CYCLE

## Slide 53: Varian RPM gating synchronization

## Slide 55: PRESSURE SENSOR GATING

## Slide 57: Camera based gating

## Slide 58: Vision RT- SGRT - GATE RT

## Slide 60: Tracking

## Slide 61: Last one – tracking the tumor

## Slide 69: Synchrony

## Slide 70: Synchrony

## Slide 72: IN SUMMARY

## Slide 73
External signal – Gating
  Amplitude based
  Phase based
Internal signal - Tracking
Breath hold is also a type of amplitude based gating

## Slide 74: Various Motion management systems

## Slide 78: MOTION MANGEMENT VIDEO

## Slide 79: WHICH MOTION MANAGEMENT SYSTEM IS BETTER?

## Slide 80: ANSWER- WHAT MANAGEMENT ACQUIRES

## Slide 81: Managing the Management

## Slide 82: Stereotaxy class

## Slide 83: Target delineation class

## Slide 84: Radiology class

## Slide 85: Neurooncology Class

## Slide 86
SRS/SBRT

## Slide 87: Kanhu
drkcpatro@gmail.com
M+91 9160470564

## Slide 88: GET THE PRESENTATION HERE ONCOEDUCATION APP
DOWNLOAD ONCOEDUCATION APP
Indian students sign up with mobile
International students sign up with e mail
APPLE/IOS CODE- LRIWPA( My Institute)
drkcpatro@gmail.com
M- +91-9160470564 www.drkanhupatro.com